PERSONAL PROTECTIVE EQUIPMENT

- Hi-vis Hardhat

- Gloves

- Stagged Pants

- Caulked Boots

SAFE PROCEDURES

A chokeman is under the direct supervision of the Rigging Slinger; the Hooktender being the supervisor of the side.

If doubtful of anything, ask the Rigging Slinger or the Hooktender.

Pull lines with your whole body, not just your arms. If too heavy for one man, get help.

Grip the line firmly with your hands so that they won't slide. This prevents a jagger wound.

Stay well away from bights and siwashes.

Stand behind the Rigging Slinger when the butt rigging is moving.

Never stand under the butt rigging when setting a choker.

Learn the proper way to set a choker. If possible, always set the choker by putting the knob over the log. Watch for the choker bell sliding down the lines.

Never stand close to the tail block or the stump, in case the strap or lines break or the stump pulls.

Learn the proper way to pack a block so that it can be thrown clear in case of tripping.

Never allow yourself to walk into a landing behind or over a pile while a loader is in the landing.

Be aware of flying chokers.

When unhooking guylines, stand on eye side of line.