PERSONAL PROTECTIVE EQUIPMENT

- Protective Leg Wear

- Hearing Protection

- Eye Protection

- Hi-vis Vest

- Hi-vis Hardhat

- Gloves

- Caulked Boots

SAFE PROCEDURES

Make sure the Yarder and Loader Operator know where you are working at all times.

Never work under the Mainline and haulback when the turn is being yarded.

Stay clear of the machine counterweight at all times.

File tangs must be bent over or a handle put on.

Always keep a firm grip on the saw.

Caution must be used to avoid kickbacks, never stand directly behind the saw. Always make sure the end of the bar does not strike an object causing a kickback. Whenever possible, avoid boring into a log.

Before starting the cut, assess the situation and decide what the log is likely to do when the cut is completed.

If the log is in an unsafe position to buck, leave it or get a machine to move it to a safer position.

Watch for side bind or spring in long logs or windfalls.

Broken ends not to be bucked on load.

Never stand behind a bucked root, it could fall back.

Watch for limbs with spring in them; they could strike you when cut off. Don't cut off limbs that may allow logs to roll on you.

Don't use power saw gas for lighting fires.

Avoid using a saw above shoulder height unless it's necessary; then caution must be used.

Maintain the saw in good working order for safety and performance.

Use a designated safe area for saw maintenance, etc.