PERSONAL PROTECTIVE EQUIPMENT

- Hi-vis Hardhat

- Hi-vis Vest

- Hearing Protection

- Eye Protection

- Leg Protection

- Caulked Boots

Responsibility to Others

Is responsible for the safety of himself and all others in or around the landing.

Is responsible for directing traffic into or through the landing.

Is responsible for directing the landing of logs when necessary.

Chasing

Keep in the clear of the turn when it is being landed (safe zone).

Be sure logs are stable before going in to unhook them.

Unhook bottom logs first and from the upper side when applicable.

Never stand under the yarding lines when a turn is being yarded.

Inspect the butt rigging regularly and report badly worn parts.

Replace badly kinked and jaggered chokers.

Ensure the yarder operator and loaderman know where you are at all times.

Do not use gas to light fires.

Keep landing area neat and tidy and equipment in good condition.

General

Do not look directly at the line when cutting.

Use a soft hammer when cutting the line.

Use eye protection when cutting the line.

Use caution when using sharp tools.

Wear leg pads whenever using a power saw.

Adequate training is required by a qualified person before using a power saw.

Check chokers for jaggers.