PERSONAL PROTECTIVE EQUIPMENT

- Caulk Boots

- Hi-vis Hardhat

- Gloves

- Stagged Pants

Responsibility to Others

A Rigging Slinger is directly responsible for the safety of the men he directs.

Ensure your crew are in a safe position at all times.

Observe and correct the unsafe work practices of your crew.

Communicate; tell them what you plan for the next turn.

Insist that your crew pay attention to the turn while it's on its way in; that way they will be alert for sliding logs, rolling rocks, flying chunks or other hazards.

Never permit the crew to work in the bight or near tailhold stumps.

Ensure that the crew is above, behind and well in the clear of every turn before giving a "go ahead" whistle.

Responsibilities in General

A Rigging Slinger is directly under the supervision of the Hooktender.

Plan your turns carefully, consider the route you will take and the logs to be choked.

Inspect the rigging and lines for loose shackles, cracks, worn or damaged eyes, burnt lines or scab straps. Inspect the chokers for jaggers.

Listen to the whistle, blow a stop immediately and correct if the wrong whistle has been given.

Be careful not to slack lines too far down without instructing loaders to watch for lines.

Do not set a turn under the pile if loading is in operation.

If rigging is hung up on a limb or sapling, clear it by slacking the rigging down before setting the turn.

Adequate training is required by a qualified person before using a power saw.

Ensure equipment operators are aware of your intentions.

Ensure equipment operators are aware of your intentions before entering a landing.

Never allow yourself or your crew to walk into a landing behind or over a pile while a loader is in the landing.

Use eye protection when cutting cable.

Slack off lines before going into hang-up.

Do not enter turn until butt rigging has been slacked to stop flying chokers.