PERSONAL PROTECTIVE EQUIPMENT

- Caulk Boots

- Hi-vis Hardhat

- Hi-vis Vest

- Gloves

- Hearing Protection as required

Review the regular spar Hooktender's Job Safety Breakdown and WCB Grapple Yarder Handbook.

Back Spar - Cat - Excavator

When threading the guylines through the tower, watch your hands in pinch points.

Watch for snags along the timber edge.

Do not sit on the mobile back spar while yarding is in progress.

Do not get too much bight on the mobile back spar.

Ensure that the mobile back spar is in proper position and secured before starting to yard.

Ensure boom is in lead and blade or bucket securely on ground.

Watch that the running lines do not dislodge trees, logs or other materials when moving the mobile back spar on steeper logging sites. The back spar operator must be in a safe location before the running lines are tightlined.

Always enter and leave machine in safe manner. Use the handholds provided.

Communications:

Use the approved voice terminology and hand signals.

Radios must be in good working condition.

When talking operator onto logs, ensure you are well clear of turn - to side and back.

Make sure you are well clear of lines – remember these machines swing.

Wear hi-vis vest/hi-vis hard hat.

Rigging

Check the rigging periodically for loose shackles in the grapple and carriage.

Rigging Backspar Trees:

When using back spars ensure that proper rigging practices are used.