PERSONAL PROTECTIVE EQUIPMENT

- Hearing Protection

- Hi-vis Hardhat

- Hi-vis Vest when off machine

- Adequate Footwear

Responsibility to Others

The Yarding Engineer's primary responsibility is to be sure that his actions do not create a hazard to the others working around him or to himself.

Checking Machine:

Make sure machine is in a safe operating condition.

Check the whistles to ensure that they are working properly.

Be sure of your footing while moving around the machine.

After using any guyline winch or when taking over a new machine, make a visual check of the guyline dogs.

Always enter and leave machine in safe manner. Use handholds for stability.

Signals:

Follow signals carefully; if in doubt about signal do not move the rigging - ask for a repeat. IF IN DOUBT – STOP!

Yarding a Turn:

Always start the turn off slowly.

Slow down the turn when coming into the landing area.

Make sure the crew and the loader are in the clear.

Keep the landing of the logs as straight as possible.

Make sure the logs are as secure as possible to minimize the danger of logs rolling onto the chaser.

Other Persons in the Cab:

No unauthorized person will be in cab while actual yarding is taking place.

Only authorized persons or those on a job-training program are allowed to run the machine.

Machine Maintenance:

Good housekeeping is a must; with emphasis on oil spills, accumulations of gear dope and fine material under the drum and winches.

Keep all guards in place.

Shut down motor and winches when doing greasing and maintenance work on them.

Lock-out/de-energize as required.

Spooling of Lines:

Be sure a proper tool is used.

No loose or ragged clothing is to be worn when spooling.

Radio Signals:

Never shut the whistle off until the crew is in the landing.